## Slide 1: Threaded Fasteners

## Slide 2: Threaded Fasteners
Of the typical fasteners, whether nails, staples, rivets, or screws, the fundamental purpose is maximize friction to hold two parts together.
In guitars the most common fastener encountered are threaded fasteners: screws.
Screws are a combination of the simple machines inclined plane, and a wheel and axle

## Slide 3: Thread Types
Sheet metal screws are used in hardwood species for guitars with acceptable results.

## Slide 4: Threaded Fasteners
Most common type of fastener you will find in the guitar
Used to hold 2 or more objects together

## Slide 5: Through Hole
Through-hole is slightly larger than the major diameter to allow fastener to slip through
Consult a drill chart for machine screws

## Slide 6: Thread Hole
A thread hole is carefully sized slightly larger than the minor diameter so the threads will grip.
If the hole is too small, the fastener will bind and break!
Consult a drill chart for machine screws

## Slide 7: Screw sizes
Screw sizes are based on their major diameter.
Screw sizes range from #00 to #12.
Larger screw sizes then begin at the ¼ diameter size

## Slide 8: Screw sizes
Screws size notation also indicates how many threads-per-inch
#8-24 would be a #8 size screw with 24 threads per inch
#6-32 x 1 would be a #6 screw with 32 TPI and one inch long.

## Slide 9: Screw Sizes
Metric screws reference the screw major diameter, pitch, and length
M2 - 0.6 x 8 would mean a 2mm diameter screw, 0.6 pitch, and 8mm length

## Slide 10: Fastener Heads & Their Drivers

## Slide 11: Fastener Heads & Their Drivers
Use care to select the proper type of driver that fully fits in to the fastener head.
Phillips are numbered #000, #00, #0, #1, #2 and so on. The wrong head and driver combination will ruin the head, driver, or both!

## Slide 12: Washers
Washers are used behind screw heads and behind nuts to spread the clamping force.
Without washers, screw heads and nuts can bury in to the material, making final tightening and later removal impossible, not to mention damaging the surface finish.